## Slide 1: IoT With ESP8266
Mr.Prarinya Ekapho

## Slide 2: Agenda for 1 days training
IoT Concept and Applications
Environment and Equipment of system
Start with Developing tools kit
Workshop#2 temperature and humidity sensor
Workshop#3 Mini project IoT 2way switch control via Smart Phone
Workshop#1 Test board NodeMCU V2

## Slide 3: IoT Concept

## Slide 4: Internet of Things (IoT) Components
Things
Sensors & Controls I/O
Internet connect devices
Data
Cloud Service

## Slide 5: IoT Development guide

## Slide 6: System Design concept

## Slide 7: About NodeMCU ESP8266
ESP8266(ESP-01)
NodeMCU Devkit 0.9 (ESP-12) Version 1
NodeMCU Devkit 1.0 (ESP-12E) Version 2
Notes: ESP8266 เป็นชื่อเรียกของชิฟของโมดูล ESP8266 สำหรับติดต่อสื่อสารบนมาตรฐาน WiFi ทำงานที่แรงดันไฟฟ้า 3.0-3.6V ทำงานใช้กระแสโดยเฉลี่ย 80mA รองรับคำสั่ง deep sleep ในการประหยัดพลังงาน ใช้กระแสน้อยกว่า 10 ไมโครแอมป์ สามารถ wake up กลับมาส่งข้อมูลใช้เวลาน้อยกกว่า 2 มิลลิวินาที ภายในมี Low power MCU 32bit ทำให้เราเขียนโปรแกรมสั่งงานได้ มีวงจร analog digital converter ทำให้สามารถอ่านค่าจาก analog ได้ความละเอียด 10bit ทำงานได้ที่อุณหภูมิ -40 ถึง 125 องศาเซลเซียส

## Slide 8: ESP8266 (ESP-01)

## Slide 9: ESP8266 (ESP-03)

## Slide 10: ESP8266 (ESP-07)

## Slide 11: ESP8266 (ESP-12E)

## Slide 12: ESP8266 NodeMCU V1 Pin layout

## Slide 13: ESP8266 NodeMCU V2 Pin layout
Notes: NodeMCU V2 เป็น ESP8266-12E รวมกับ USB TTL ที่ใช้ชิฟ CP2102 และขยายขาให้สามารถต่อทดลองได้ง่ายขึ้น มีปุ่ม reset และ flash สำหรับใช้โปรแกรม โดยใช้ Arduino IDE หรือโปรแกรมอื่น ๆ ได้อย่างสะดวก

## Slide 14: ESP8266 NodeMCU V3 Pin layout
Notes: NodeMCU V3 เป็นบอร์ดทีคล้ายกับ NodeMCU V2 ที่ต่างกันคือ NodeMCU V3 จะมีขนาดกว้างกว่า และใช้ชิฟ USB TTL เป็น CH340 ซึ่งการต่อขาใช้งานและโคดโปรแกรมเหมือนกันทุกประการ

## Slide 15: WeMos D1
Notes: ออกแบบให้คล้ายบอร์ด Arduino Uno ใช้ ESP8266-12E เป็นตัวหลัก ชิฟ CH340 เป็นภาค USB TTL รองรับไฟ 9-12V ที่ช่อง Adapter , รองรับไฟ 5V ที่ช่อง micro usb และ 3.3V ที่ช่อง VIN

## Slide 16: WeMos D1 Mini
Notes: แปลงบอร์ด Wemos D1 ให้มีขนาดเล็กลง โดยการแยกส่วน usb ttl และ ESP8266-12E ข้อดีคือ เวลาใช้งานจริงสามารถถอดเฉพาะส่วน ESP8266-12E ไปใช้งาน ก็จะทำให้ประหยัดไฟได้นิดหน่อย

## Slide 17: Witty cloud Mini NodeMCU
Notes: แปลงบอร์ด Wemos D1 ให้มีขนาดเล็กลง โดยการแยกส่วน usb ttl และ ESP8266-12E ข้อดีคือ เวลาใช้งานจริงสามารถถอดเฉพาะส่วน ESP8266-12E ไปใช้งาน ก็จะทำให้ประหยัดไฟได้นิดหน่อย

## Slide 18: Sensor & control modules

## Slide 19: Sensor & control modules

## Slide 20: Basic electronic devices
Resistor

## Slide 21: Basic electronic devices
Capacitor

## Slide 22: Basic electronic devices
Diode
LED

## Slide 24: Tools for Develop
Arduino IDE and SDK for ESP8266
CP2012 USB to UART driver
Web Browser: Chrome or Firefox
1
2
3

## Slide 25: Arduino IDE and SDK for ESP8266
Download and Install Arduino IDE
https://www.arduino.cc/en/Main/Software
Additional Board Manager URLs
http://arduino.esp8266.com/stable/package_esp8266com_index.json
Check Install ESP8266 in Boards Manager… Menu
esp8266 by ESP8266 Community version 2.3.0 INSTALLED

## Slide 26: CP2012 USB to UART driver
https://www.silabs.com/products/mcu/Pages/USBtoUARTBridgeVCPDrivers.aspx

## Slide 27: Workshop#1 Start learning ESP8266 with Arduino IDE
    Blink
    WiFi Scan
    Web server

## Slide 28: Workshop#1 Prepare hardware snap in breadboard

## Slide 29: Workshop#1 [test board with blink]
void setup() {
pinMode(LED_BUILTIN, OUTPUT); // Initialize the LED_BUILTIN pin as an output
}
// the loop function runs over and over again forever
void loop() {
digitalWrite(LED_BUILTIN, LOW); // Turn the LED on (Note that LOW is the voltage level
// but actually the LED is on; this is because
// it is acive low on the ESP-01)
delay(1000); // Wait for a second
digitalWrite(LED_BUILTIN, HIGH); // Turn the LED off by making the voltage HIGH
delay(2000); // Wait for two seconds (to demonstrate the active low LED)
}

## Slide 30: Workshop#1 [Wifi scan] - sketch
#include "ESP8266WiFi.h" void setup() { Serial.begin(115200); // Set WiFi to station mode and disconnect from an AP if it was previously connected WiFi.mode(WIFI_STA); WiFi.disconnect(); delay(100); Serial.println("Setup done"); } void loop() { Serial.println("scan start"); // WiFi.scanNetworks will return the number of networks found int n = WiFi.scanNetworks(); Serial.println("scan done"); if (n == 0) Serial.println("no networks found"); else | { Serial.print(n); Serial.println(" networks found"); for (int i = 0; i < n; ++i) { // Print SSID and RSSI for each network found Serial.print(i + 1); Serial.print(": "); Serial.print(WiFi.SSID(i)); Serial.print(" ("); Serial.print(WiFi.RSSI(i)); Serial.print(")"); Serial.println((WiFi.encryptionType(i) == ENC_TYPE_NONE)?" ":"*"); delay(10); } } Serial.println(""); // Wait a bit before scanning again delay(5000); }

## Slide 31: Workshop#1 [Wifi scan] – serial monitor

## Slide 32: Workshop#1 [wifiWeb server] – sketch
#include <ESP8266WiFi.h> const char* ssid = “your-ssid"; const char* password = “your-password"; // Create an instance of the server // specify the port to listen on as an argument WiFiServer server(80); void setup() { Serial.begin(115200); delay(10); // prepare GPIO2 pinMode(2, OUTPUT); digitalWrite(2, 0); // Connect to WiFi network Serial.println(); Serial.println(); Serial.print("Connecting to "); Serial.println(ssid); | WiFi.begin(ssid, password); while (WiFi.status() != WL_CONNECTED) { delay(500); Serial.print("."); } Serial.println(""); Serial.println("WiFi connected"); // Start the server server.begin(); Serial.println("Server started"); // Print the IP address Serial.println(WiFi.localIP()); }

## Slide 33: Workshop#1 [wifiWeb server] – sketch
void loop() { // Check if a client has connected WiFiClient client = server.available(); if (!client) { return; } // Wait until the client sends some data Serial.println("new client"); while(!client.available()){ delay(1); } // Read the first line of the request String req = client.readStringUntil('\r'); Serial.println(req); client.flush(); // Match the request int val; if (req.indexOf("/gpio/0") != -1) val = 0; else if (req.indexOf("/gpio/1") != -1) val = 1; else { Serial.println("invalid request"); client.stop(); return; } | // Set GPIO2 according to the request digitalWrite(2, val); client.flush(); // Prepare the response String s = "HTTP/1.1 200 OK\r\nContent-Type: text/html\r\n\r\n<!DOCTYPE HTML>\r\n<html>\r\nGPIO is now "; s += (val)?"high":"low"; s += "</html>\n"; // Send the response to the client client.print(s); delay(1); Serial.println("Client disonnected"); // The client will actually be disconnected // when the function returns and 'client' object is detroyed }

## Slide 34: Workshop#1 [wifiWeb server] – sketch GPIO5
#include <ESP8266WiFi.h> const char* ssid = “your-ssid"; const char* password = “your-password"; // Create an instance of the server // specify the port to listen on as an argument WiFiServer server(80); void setup() { Serial.begin(115200); delay(10); // prepare GPIO5 pinMode(5, OUTPUT); digitalWrite(5, 0); // Connect to WiFi network Serial.println(); Serial.println(); Serial.print("Connecting to "); Serial.println(ssid); | WiFi.begin(ssid, password); while (WiFi.status() != WL_CONNECTED) { delay(500); Serial.print("."); } Serial.println(""); Serial.println("WiFi connected"); // Start the server server.begin(); Serial.println("Server started"); // Print the IP address Serial.println(WiFi.localIP()); }

## Slide 35: Workshop#1 [wifiWeb server] – sketch GPIO5
void loop() { // Check if a client has connected WiFiClient client = server.available(); if (!client) { return; } // Wait until the client sends some data Serial.println("new client"); while(!client.available()){ delay(1); } // Read the first line of the request String req = client.readStringUntil('\r'); Serial.println(req); client.flush(); // Match the request int val; if (req.indexOf("/gpio/0") != -1) val = 0; else if (req.indexOf("/gpio/1") != -1) val = 1; else { Serial.println("invalid request"); client.stop(); return; } | // Set GPIO5 according to the request digitalWrite(5, val); client.flush(); // Prepare the response String s = "HTTP/1.1 200 OK\r\nContent-Type: text/html\r\n\r\n<!DOCTYPE HTML>\r\n<html>\r\nGPIO is now "; s += (val)?"high":"low"; s += "</html>\n"; // Send the response to the client client.print(s); delay(1); Serial.println("Client disonnected"); // The client will actually be disconnected // when the function returns and 'client' object is detroyed }

## Slide 36: Workshop#1 [wifiWeb server] – serial monitor

## Slide 37: Workshop#1 [wifiWeb server] – web browser

## Slide 38: Workshop#1 [helloserver]

## Slide 39: Workshop#1 [helloserver]

## Slide 40: Workshop#1 [helloserver]-serial monitor

## Slide 41: Workshop#1 [helloserver]-web browser

## Slide 42: Workshop#2 upload data to cloud (thinkspeak)
    Apply Thinkspeak
    Test send data
    Customize visual board

## Slide 43: Workshop#2 Apply Thinkspeak
1
Register Thingspeak
2
Create New Channel
3
Receive API Key
4
Use API Key send data to server

## Slide 44: Workshop#2 Apply Thinkspeak

## Slide 45: Workshop#2 Apply Thinkspeak

## Slide 46: Workshop#2 Apply Thinkspeak

## Slide 47: Workshop#2 Create New Channel

## Slide 48: Workshop#2 Create New Channel

## Slide 49: Workshop#2 Create New Channel

## Slide 50: Workshop#2 Create New Channel

## Slide 51: Workshop#2 connect hardware

## Slide 52: Workshop#2 sketch for test
#include "DHT.h" #include <ESP8266WiFi.h> #define PUMP_RLY 4 // output drive relay for pump GPIO4 (D2) #define DHTPIN 2 // what pin we're connected to GPIO2 (D4) #define DHTTYPE DHT11 // DHT 11 #define DEBUG #define DEBUG_PRINTER Serial #ifdef DEBUG #define DEBUG_PRINT(...) { DEBUG_PRINTER.print(__VA_ARGS__); } #define DEBUG_PRINTLN(...) { DEBUG_PRINTER.println(__VA_ARGS__); } #else #define DEBUG_PRINT(...) {} #define DEBUG_PRINTLN(...) {} #endif const char* ssid = “SSID"; //Use own ssid const char* password = “PASSWORD"; //use password of AP DHT *dht; void connectWifi(); void reconnectWifiIfLinkDown(); void initDht(DHT **dht, uint8_t pin, uint8_t dht_type); void readDht(DHT *dht, float *temp, float *humid); void uploadThingsSpeak(float t, float h); | void setup() { Serial.begin(115200); delay(10); pinMode(PUMP_RLY, OUTPUT); // Initialize the PUMP_RLY(4) pin as an output digitalWrite(PUMP_RLY, HIGH);// Make sure relay is normal off connectWifi(); initDht(&dht, DHTPIN, DHTTYPE); } void loop() { static float t_dht; static float h_dht; readDht(dht, &t_dht, &h_dht); if(h_dht < 30 ¦¦ t_dht > 26) // condition for make relay on { digitalWrite(PUMP_RLY, LOW); //If condition true do this! } else { digitalWrite(PUMP_RLY, HIGH); } uploadThingsSpeak(t_dht, h_dht); // Wait a few seconds between measurements. delay(10 * 1000); reconnectWifiIfLinkDown(); }

## Slide 53: Workshop#2 sketch for test
void reconnectWifiIfLinkDown() { if (WiFi.status() != WL_CONNECTED) { DEBUG_PRINTLN("WIFI DISCONNECTED"); connectWifi(); } } void connectWifi() { DEBUG_PRINTLN(); DEBUG_PRINTLN(); DEBUG_PRINT("Connecting to "); DEBUG_PRINTLN(ssid); WiFi.begin(ssid, password); while (WiFi.status() != WL_CONNECTED) { delay(500); DEBUG_PRINT("."); } DEBUG_PRINTLN(""); DEBUG_PRINTLN("WiFi connected"); DEBUG_PRINTLN("IP address: "); DEBUG_PRINTLN(WiFi.localIP()); } void initDht(DHT **dht, uint8_t pin, uint8_t dht_type) { // Connect pin 1 (on the left) of the sensor to +5V // NOTE: If using a board with 3.3V logic like an Arduino Due | connect pin 1 // to 3.3V instead of 5V! // Connect pin 2 of the sensor to whatever your DHTPIN is // Connect pin 4 (on the right) of the sensor to GROUND // Connect a 10K resistor from pin 2 (data) to pin 1 (power) of the sensor // Initialize DHT sensor for normal 16mhz Arduino // NOTE: For working with a faster chip, like an Arduino Due or Teensy, you // might need to increase the threshold for cycle counts considered a 1 or 0. // You can do this by passing a 3rd parameter for this threshold. It's a bit // of fiddling to find the right value, but in general the faster the CPU the // higher the value. The default for a 16mhz AVR is a value of 6. For an // Arduino Due that runs at 84mhz a value of 30 works. // Example to initialize DHT sensor for Arduino Due: //DHT dht(DHTPIN, DHTTYPE, 30); *dht = new DHT(pin, dht_type, 30); (*dht)->begin(); DEBUG_PRINTLN(F("DHTxx test!")) ; }

## Slide 54: Workshop#2 sketch for test
void uploadThingsSpeak(float t, float h) { static const char* host = "api.thingspeak.com"; static const char* apiKey = “YOUR_APIKEY"; // Use WiFiClient class to create TCP connections WiFiClient client; const int httpPort = 80; if (!client.connect(host, httpPort)) { DEBUG_PRINTLN("connection failed"); return; } // We now create a URI for the request String url = "/update/"; // url += streamId; url += "?key="; url += apiKey; url += "&field1="; url += t; url += "&field2="; url += h; DEBUG_PRINT("Requesting URL: "); DEBUG_PRINTLN(url); // This will send the request to the server client.print(String("GET ") + url + " HTTP/1.1\r\n" + "Host: " + host + "\r\n" + "Connection: close\r\n\r\n"); } | void readDht(DHT *dht, float *temp, float *humid) { if (dht == NULL) { DEBUG_PRINTLN(F("[dht11] is not initialised. please call initDht() first.")); return; } // Reading temperature or humidity takes about 250 milliseconds! // Sensor readings may also be up to 2 seconds 'old' (its a very slow sensor) float h = dht->readHumidity(); // Read temperature as Celsius float t = dht->readTemperature(); // Read temperature as Fahrenheit float f = dht->readTemperature(true); // Check if any reads failed and exit early (to try again). if (isnan(h) ¦¦ isnan(t) ¦¦ isnan(f)) { DEBUG_PRINTLN("Failed to read from DHT sensor!"); return; }

## Slide 55: Workshop#2 sketch for test
// Compute heat index // Must send in temp in Fahrenheit! float hi = dht->computeHeatIndex(f, h); DEBUG_PRINT("Humidity: "); DEBUG_PRINT(h); DEBUG_PRINT(" %\t"); DEBUG_PRINT("Temperature: "); DEBUG_PRINT(t); DEBUG_PRINT(" *C "); DEBUG_PRINT(f); DEBUG_PRINT(" *F\t"); DEBUG_PRINT("Heat index: "); DEBUG_PRINT(hi); DEBUG_PRINTLN(" *F"); *temp = t; *humid = h; } | 

## Slide 56: Customize visual board

## Slide 57: Customize visual board

## Slide 58: Workshop#3 Mini Project 2Way IoT Switch

## Slide 59: Workshop#3 Control IoT via Blynk

## Slide 60: Workshop#3 Control IoT via Blynk

## Slide 61: Workshop#3 Control IoT via Blynk

## Slide 62: Workshop#3 Control IoT via Blynk

## Slide 63: Workshop#3 Control IoT via Blynk

## Slide 64: Workshop#3 Control IoT via Blynk
#define BLYNK_PRINT Serial // Comment this out to disable prints and save space #include <ESP8266WiFi.h> #include <BlynkSimpleEsp8266.h> // You should get Auth Token in the Blynk App. // Go to the Project Settings (nut icon). char auth[] = "7c66a2b373a148b8a9b9470a0da38f87"; // Your WiFi credentials. // Set password to "" for open networks. char ssid[] = "comptia"; char pass[] = "comptiatc"; void setup() { Serial.begin(115200); Blynk.begin(auth, ssid, pass); } void loop() { Blynk.run(); } | 

## Slide 65: Workshop#3 Temp Control IoT via Blynk

## Slide 66: Workshop#4 Control IoT via Blynk
#define BLYNK_PRINT Serial // Comment this out to disable prints and save space #include <ESP8266WiFi.h> #include <BlynkSimpleEsp8266.h> #include <SimpleTimer.h> #include <Adafruit_Sensor.h> #include <DHT.h> #include <DHT_U.h> #define DHTPIN 12 #define DHTTYPE DHT11 DHT_Unified dht(DHTPIN, DHTTYPE); char auth[] = "8c028718194743109fd45f2fb720cc14"; SimpleTimer timer; void setup() { Serial.begin(115200); Blynk.begin(auth, "comptia", "comptiatc"); dht.begin(); | // Setup a function to be called every second timer.setInterval(5000L, sendUptime); } void sendUptime() { Blynk.virtualWrite(V5, millis() / 1000); sensors_event_t event; dht.temperature().getEvent(&event); if (!isnan(event.temperature)) { Blynk.virtualWrite(V1, event.temperature); } dht.humidity().getEvent(&event); if (!isnan(event.relative_humidity)) { Blynk.virtualWrite(V2, event.relative_humidity); } } void loop() { Blynk.run(); timer.run(); }

## Slide 67: Question….

## Slide 68: Further resources
https://www.arduino.cc/
https://thingspeak.com/
https://netpie.io/
https://espressif.com/en/products/hardware/esp8266ex/overview
http://www.esp8266.com/
http://www.blynk.cc/
https://www.rs-online.com/designspark/rs-toolbox

## Slide 69: Course feedback and instructor evaluation

## Slide 70: Final Question….
Email: prarinya.e@gmail.com